## Slide 1: Servo Motors

## Slide 2: What is a servo?
Servo motors are small, to precisely efficient motors which are used to precisely control the angle of turning.
The servo circuitry is built right inside the motor unit and has a positionable shaft, which usually is fitted with a gear. The motor is controlled with an electric signal which determines the amount of movement of the shaft.

## Slide 3: Working of a Servo
A servo has a DC (usually) motor, a potentiometer, and a control circuit.
The motor is attached by gears to the control wheel.
As the motor rotates, the potentiometer's resistance changes, so the control circuit can precisely regulate how much movement there is and in which direction.
Ususally, a servo has a range of motion 180 degrees.

## Slide 4: …Continued
When the shaft of the motor is at the desired position, power supplied to the motor is stopped. If not, the motor is turned in the appropriate direction.
The motor's speed is proportional to the difference between its actual position and desired position. So if the motor is near the desired position, it will turn slowly, otherwise it will turn fast. This is called proportional control.

## Slide 5: Servo Control
The defining factor of a servo is the amount of control we have over it.
The basic level of control over a usual servo is over the angle it rotates till.
The desired position is sent via electrical pulses through the signal wire

## Slide 6: Control Mechanism
Servos are controlled by sending an electrical pulse of variable width, or pulse width modulation (PWM), through the control wire.
A servo motor can usually only turn 90° in either direction for a total of 180° movement. The motor's neutral position is defined as the position where the servo has the same amount of potential rotation in the both the clockwise or counter-clockwise direction.

## Slide 7: …Continued
The PWM sent to the motordetermines position of the shaft, and based on the duration of the pulse sent via the control wire
The servo motor expects to see a pulse every 20 milliseconds (ms) and the length of the pulse will determine how far the motor turns.
A pulse width of 127 will make the motor turn to the neutral position (90 degrees). 255 will turn to 180, 0 to 0 degrees.

## Slide 8
When these servos are commanded to move, they will move to the position and hold that position.
If an external force pushes against the servo while the servo is holding a position, the servo will resist from moving out of that position. The maximum amount of force the servo can exert is called the torque rating of the servo.
Servos will not hold their position forever though; the position pulse must be repeated to instruct the servo to stay in position.